Progress Notes For Week 13 :: 15/01/07 – 21/01/07

Actual date of this Report Preparation: 23/01/07

Student Name: Mr Michael J Curry

Project Supervisor: Mr Chris S Knight

Project Title: Embedded Room-By-Room Heating Control System

Main Achievements during the week identified above:

- Final component required source located, ordered and received

- Established communications (if not 100% successful) between device and In-Circuit Debugger

- Discovered the ENC28J60’s core voltage regulator can power the PIC18LF45J10’s core (Vddcore)

Outstanding Problems

- Identify and use a 3V-5V logic level shifter for ICD2 clone

- Download test code to the device and validate successfully

- Finish building the test board for the room node

- Become familiar with SPI and TC77 serial temperature sensor

- Compile, debug & test microchip TCP/IP stack for hardware setup

- Use microchip TCP/IP stack to allow current temperature to be reported

- Use microchip TCP/IP stack to allow temperature set-point to be adjusted remotely

- Build ‘room’ to allow testing of the temperature control

- Fully test (complete) prototype node

- Design room node PCB from prototype circuit

- Design build and test central webserver node

- Build second room node (time permitting)

Realistic (Measurable) targets to be achieved during the next week period:

- Identify and implement a suitable 3V-5V logic level shifter

- Send a test programme to the device, validate code and step through line-by-line using the ICD2 module with MPLAB

- Add the extra components required by the board to potentially allow 10Base-T Ethernet communications

Hours and materials and external resources spent on the project during this week:

15 hours

Cumulative committed spend to date (total of hours and materials and external resources used to date):

75 hours, 4x ENC28J60 SPI Ethernet controllers, 3x PIC18LF45J10 MCUs, 5x TC-77-3.3 SPI temp sensors, 5x MSOP to DIL adaptors, 3x RJ-11 Sockets, 3x 5V coil mains relays, 10x 25MHz crystals, 10x ferrite beads, 2x MAX233 chips, 5x 9-way d-sub sockets, 4x RJ-45 sockets with integrated 1:1 ‘tab-down’ magnetics