Progress Notes For Week 18 :: 19/02/07 – 25/02/07

Actual date of this Report Preparation:

Student Name: Mr Michael J Curry

Project Supervisor: Mr Chris S Knight

Project Title: Embedded Room-By-Room Heating Control System

Main Achievements during the week identified above:

- Interfaced MAX233 & 9-way D-sub connector (to monitor config messages)

- Built the v4.00RC microchip tcp/ip

  - Could not get it to fit on the p18lf45j10 so supplemented the p18f4685 (same pin outs & already had some ordered from the microchip samples)

- Began writing code to read temperature from the TC77 thermal sensor

  - No consistent results returned, suspected problem with SPI timing getting the 2 bytes

- Rose a new support ticket with microchip regarding the v4.00RC beta tcp/ip stack not working

Outstanding Problems

- Finish building the test board for the room node (mains relay)

- Get a reading from the TC77 thermal sensor & convert to a temperature

- Compile, debug & test microchip TCP/IP stack for hardware setup

- Use microchip TCP/IP stack to allow current temperature to be reported

- Use microchip TCP/IP stack to allow temperature set-point to be adjusted remotely

- Build ‘room’ to allow testing of the temperature control

- Fully test (complete) prototype node

- Design room node PCB from prototype circuit

- Design build and test central webserver node

- Build second room node (time permitting)

Realistic (Measurable) targets to be achieved during the next week period:

- Interface relay to board & mains bulb (& test)

- Get code to read the TC77 correctly (separately until working stack built)

- Pursue microchip support ticket regarding the tcp/ip stack not working properly

- Update circuit diagram for the p18f4685 & mains relay

Hours and materials and external resources spent on the project during this week:

15 hours

Cumulative committed spend to date (total of hours and materials and external resources used to date):

125 hours, 4x ENC28J60 SPI Ethernet controllers, 3x PIC18LF45J10 MCUs, 5x TC-77-3.3 SPI temp sensors, 5x MSOP to DIL adaptors, 3x RJ-12 Sockets, 3x 5V coil mains relays, 10x 25MHz crystals, 10x ferrite beads, 2x MAX233 chips, 5x 9-way d-sub sockets, 4x RJ-45 sockets with integrated 1:1 ‘tab-down’ magnetics, 3x Green LEDs, 3x Orange LEDs, 3x NPN transistors, various resistors, various capacitors, 3x PIC18F4685 MCUs