Progress Notes For Week 19 :: 26/02/07 – 04/03/07

Actual date of this Report Preparation:

Student Name: Mr Michael J Curry

Project Supervisor: Mr Chris S Knight

Project Title: Embedded Room-By-Room Heating Control System

Main Achievements during the week identified above:

- Identified the TC77 / adaptor board being faulty and being the cause for the TCP/IP stack not to function properly.

- Successfully sent and received packets from the device (ARP, ICMP echo, HTTP, telnet, netbios)

- Successfully received data from the device using RS232, to debug incoming readings from the TC77

Outstanding Problems

- Finish building the test board for the room node (mains relay)

- Get a reading from the TC77 thermal sensor & convert to a temperature

- Use microchip TCP/IP stack to allow current temperature to be reported

- Use microchip TCP/IP stack to allow temperature set-point to be adjusted remotely

- Build ‘room’ to allow testing of the temperature control

- Fully test (complete) prototype node

- Design room node PCB from prototype circuit

- Design build and test central webserver node

- Build second room node (time permitting)

Realistic (Measurable) targets to be achieved during the next week period:

- Re-solder RJ-45 socket (a couple of loose connections)

- Interface relay to board & mains bulb (& test)

- Solder a new TC77 to a new adaptor board and test

- Get code to read the TC77 correctly (separately until working stack built)

- Update circuit diagram for the p18f4685 & mains relay

- Allow variables to be set, using the GenericTCPServer module as a base

Hours and materials and external resources spent on the project during this week:

15 hours

Cumulative committed spend to date (total of hours and materials and external resources used to date):

125 hours, 4x ENC28J60 SPI Ethernet controllers, 3x PIC18LF45J10 MCUs, 5x TC-77-3.3 SPI temp sensors, 5x MSOP to DIL adaptors, 3x RJ-12 Sockets, 3x 5V coil mains relays, 10x 25MHz crystals, 10x ferrite beads, 2x MAX233 chips, 5x 9-way d-sub sockets, 4x RJ-45 sockets with integrated 1:1 ‘tab-down’ magnetics, 3x Green LEDs, 3x Orange LEDs, 3x NPN transistors, various resistors, various capacitors, 3x PIC18F4685 MCUs